## Slide 1: CS 5600 Computer Systems
Lecture 3: Hardware, CPUs, and a Basic Operating System

## Slide 2: What is an Operating System?
An OS is any and all software that sits between a user program and the hardware
Hardware (e.g., mouse, keyboard)
User Program
Operating System
OS is a resource manager and allocator
  Decides between conflicting requests for hardware access
  Attempts to be efficient and fair
OS is a control program
  Controls execution of user programs
  Prevents errors and improper use

## Slide 3
Hardware (e.g., mouse, keyboard)
Text Editor
Operating System
Command Line Shell
GUI

## Slide 4: Many Different OSes
Windows
Linux
BSD

## Slide 5: Goals for Today
By the end of class, we will build a very, very simple command line OS
But to get there, we need to understand the hardware platform we are building on
  Basics of PC architecture
  How devices and the CPU communicate
  What is the basic functionality of the CPU
  How do we boot into an OS

## Slide 6
Hardware Basics
PC Bootup Sequence
A Simple OS Example
Kernels

## Slide 7: Basic Computer Architecture
Architecture determines many properties of the OS
  How does the OS load and take control?
  How does the OS interacts with devices?
  How does the OS manage CPU and memory?
This discussion will focus on the IBM PC architecture
  Until recently, most computers could still run MS-DOS based programs from the 80’s and 90’s
  Remains the most popular architecture
    But not for long…
  Alternatives: Amiga, Macintosh, PowerPC, etc.

## Slide 8: Some History
1981: IBM releases a Personal Computer (PC) to compete with Apple
  Basic Input/Output System (BIOS) for low-level control
  Three high-level OSes, including MS-DOS
  Developers were asked to write software for DOS or BIOS, not bare-metal hardware
1982: Compaq and others release IBM-compatible PCs
  Different hardware implementations (except 808x CPU)
  Reverse engineered and reimplemented BIOS
  Relied on customized version of MS-DOS

## Slide 10: IBM Loses Control
1985: IBM clones dominated computer sales
  Used the same underlying CPUs and hardware chips
  Close to 100% BIOS compatibility
  MS-DOS was ubiquitous
  Thus, IBM PC hardware became the de-facto standard
1986: Compaq introduces 80386-based PC
1990’s: Industry is dominated by “WinTel”
  Intel x86 CPU architectures (Pentium 1, 2, and 3)
  Windows 3.1, NT, 95 software compatibility

## Slide 11
CPU Socket
Many different physical socket standards
  This a Pentium 1 socket
Physical standard is less important than Instruction Set Architecture (ISA)
  IBM PCs are Intel 80836 compatible
  Original x86 design
  Intel, AMD, VIA
Today’s dominant ISA: x86-64, developed by AMD

## Slide 12
Slots for random access memory (RAM)
Pre-1993: DRAM (Dynamic RAM)
Post-1993: SDRAM (Synchronous DRAM)
Current standard: Double data rate SDRAM (DDR SDRAM)
North Bridge
Coordinates access to main memory

## Slide 13
Built in I/O also on the PCI/ISA bus
I/O device slots
Attached to the south-bridge bus
Very old standard: ISA slots
Slightly less old standard: PCI slots
Other types:
  AGP slots
  PCI-X slots
South-bridge
Facilitates I/O between devices, the CPU, and main memory

## Slide 14
Storage connectors
  Also controlled by the South Bridge
Old standard: Parallel ATA (P-ATA)
  AT Attachment Packet Interface (ATAPI)
  Evolution of the Integrated Drive Electronics (IDE) standard
Other standards
  Small Computer System Interface (SCSI)
  Serial ATA (SATA)

## Slide 15
PCI-x16 slots
PCI slot
SATA Plugs
South Bridge
North Bridge
USB Headers
RAM Slots
CPU socket
PATA Connectors

## Slide 16
North/South Bridge
Graphics
Graphics Memory
I/O
I/O
I/O
…
Memory
CPU(s)
L1, L2, L3 Cache
All devices compete for access to memory

## Slide 17: x86 History
1978: Intel 8086 – 16 bit
1982: Intel 80286 – introduces protected mode and memory paging
1985: Intel 80386 – 32 bit
1989: Intel 80486 – integrates x87 FPU and cache
1993: Pentium and Pentium MMX
1997, 1999: Pentium II and III
2003, 2004: AMD Athlon 64 and Pentium 4
  AMD pioneers the move to 64 bit x86-64

## Slide 18: Basic CPU Layout
Main Memory
System Bus
L1 (and L2, L3) Cache
Instruction Fetch
Decode
Control Unit
Floating Point (FPU)
Arithmetic and Logic (ALU)
Arithmetic and Logic (ALU)
Registers

## Slide 20: Registers
Storage built in to the CPU
  Can hold values or pointers
  Instructions operate directly on registers
  Things from memory can be loaded into registers…
  … or things in registers can be moved to memory
Some registers have special functions
  Pointing to the current instruction in memory
  Pointing to the top of the stack
  Configuring low-level CPU features
  Etc.

## Slide 21: Storage Hierarchy
Larger / Slower
Smaller / Faster
CPU Registers
CPU L1/L2/L3 Cache
Main Memory (RAM)
Solid State Drive (SSD)
Hard Drive
Tape Drive
1KB
1 - 32MB
4 - 256GB
32 GB – 1 TB
512 GB – 4 TB
1 – 8 TB

## Slide 22: x86 Registers (32 bit)
General purpose registers
  EAX, EBX, ECX, EDX
  Used for pretty much anything
Stack registers
  ESP: Points to the top of the stack
    The stack grows down, so this is the lowest address
  EBP: Points to the bottom of the current stack frame
    Not strictly necessary, may be used as a general purpose register
Other registers
  EIP: Points to the currently executing instruction
  EFLAGS: Bit vector of flags
    Stores things like carry (after addition), equals zero (after a comparison), etc.

## Slide 23: Register Layout
x86 has gone through 16, 32, and 64 bit versions
Registers can be addressed in whole or in part
RAX
EAX
AX
AH
AL
64 bits
32 bits
16 bits
8 bit high and low

## Slide 24: x86 Assembly Examples
mov eax, 0x00ABCDE ; move 32-bit value to EAX
mov ax, 0xABCD ; move 16-bit value to AX
mov ah, 0xAB
mov al, 0xCD ; 3) + 4) are equivalent to 2)
add eax, ebx ; result stored in EAX
mov edx, [esp] ; dereference the pointer in ESP, move the value to EDX

## Slide 25: Important x86 Instructions
Instructions | Description | Examples
mov | Move data from one place to another | mov eax, 7 mov edx, [0xF0FF] mov [ebx], eax
add / sub | Add / subtract values in registers | add eax, ebx
inc / dec | Increment / decrement the value in a register | inc eax
call | Push EIP onto the stack and jump to a function | call 0x80FE4C
ret | Pop the top of the stack into EIP | ret
push / pop | Add or remove items to the stack | push eax
int | Execute the given interrupt handler | int 0x80
jmp | Load the given value into EIP | jmp 0x80FE4C
cmp | Compare the value of two registers and store the value in the flags register | cmp ebx, edx
jxx | Load the given value into EIP if the condition is met | jz 0x80FE4C jnz 0x80FE4C
In Intel assembly syntax, [] means dereference (e.g. *ptr in C)
Basics
Func.
Stack
Control Flow

## Slide 26: Typical Memory Layout
Example: 64KB of memory
  216 bytes
  Addresses from 0 to 65535
Not all memory is free
  Specific ranges get used by devices, system services, the BIOS, etc.
Memory mapped devices
Free Memory
BIOS Code
Interrupt Vector
0x0000
0x00FF
0x0DFF
0xF000
0xFFFF
Top
Bottom

## Slide 27: Memory Addressing
Address | Value
0xC7 | 0x00
0xC6 | 0x00
0xC5 | 0x10
0xC4 | 0x05
0xC3 | 0x00
0xC2 | ‘c’
0xC1 | ‘b’
0xC0 | ‘a’
mov ah, [0xC0] ; AH = ‘a’
mov ax, [0xC4] ; AX = 0x0510
Memory can be addressed as:
  Individual bytes
  Multi-byte words, double words, quad words, etc.

## Slide 28: Communicating with Devices
CPU and devices execute concurrently
How do CPU and devices communicate?
  I/O Ports
    I/O-only memory space shared by the CPU and a device
  Memory mapping
    Regions of RAM that are shared by the CPU and a device
  Interrupts
    Signal from a device to the CPU
    Interrupt causes the OS to switch to handler code

## Slide 29
Shared Memory
Interrupt
I/O Ports

## Slide 30: I/O Ports
Oldest method of interacting with devices
CPU and devices share a virtual 16-bit memory space
  Each device is assigned some portion of the address space
  E.g. 0xF000 – 0xF03F
CPU and device communicate by reading/writing to the virtual memory space

## Slide 31: I/O Port Example
Output
mov eax, 1
mov dx, 0x3F8
start: out dx, al
inc eax
cmp eax, 32
jne start
…
Input
mov ebx, 0
mov dx, 0x3F8
start: in dx, ax
mov [esp + ebx], ax
inc ebx
cmp ebx, 31
jle start
…
Assume there is a serial port attached to port 0x3F8

## Slide 32: Problem With I/O Ports
CPU must mediate all transfers
  Suppose you want to move data from disk to memory…
  CPU must copy each 16-bit value from the I/O port to memory
All I/O must be synchronous
  Suppose the disk wants to send data…
  … but the CPU isn’t reading the I/O port with in
Bottom line: I/O ports are slow

## Slide 33: Memory Mapped Devices
RAM shared by the CPU and a device
Example: Console frame buffer
  Address range of 1920 bytes
  Corresponds to 24 lines of text, 80 characters wide
  CPU writes characters into the memory range…
  … Video hardware displays them on the screen
Address | Value
0xC2 | ‘e’
0xC1 | ‘h’
0xC0 | ‘T’

## Slide 34: Example Keyboard Controller
Simple, memory mapped keyboard interface
  2 bytes: keycode byte and status byte
When a key is pressed:
  The keycode byte is set to the character
  The status byte is set to 1
When the key is read:
  CPU sets the status byte to 0
Address | Purpose
0xF801 | keycode
0xF800 | status

## Slide 35: Direct Memory Access (DMA)
Enables devices to transfer blocks of data directly to memory
  Interrupt generated when transfer is completed
Much faster than the alternative method
  Interrupt generated after each byte is transferred

## Slide 36: DMA in Action
Device
Memory
(Instructions and Data)
CPU(s)
Data via DMA
Data via
I/O Ports
Interrupts
Data
Instructions

## Slide 37: Interrupts
Interrupts transfer control from the running code to an interrupt handler
  Each interrupt is assigned a number
  Number acts as an index into the Interrupt Vector Table
  Table maps interrupt numbers to handlers
Interrupts cause a context switch
  State of the CPU must be saved before the switch…
  … and restored after the handler completes
Interrupt Vector
0x0000
0x00FF
0xFFFF
Main Memory
Interrupt Number | Pointer to Handler
0x02 | 0x0000
0x01 | 0xA146
0x01 Handler
0xA146

## Slide 38: Interrupt Timeline
Time
CPU
I/O Device
User Process
Interrupt Handler
Idle
Transferring
file.read();
file.read();
Read done, raise interrupt
Read done, raise interrupt
Context Switch
Interrupts are an example of asynchronous messaging
Interrupts enable the CPU and devices to work in parallel

## Slide 39: Today’s Servers/Desktops
Much greater homogeneity/compatibility
  Apple and PC use the same internals
  Powerful industry groups ratify strict standards for hardware compatibility
    Joint Electron Device Engineering Council (JEDEC)
    PCI Special Interest Group (PCI SIG)
    USB Implementors Forum (USB-IF)
No longer IBM-PC compatible
  x86-64
  Unified Extensible Firmware Interface (UEFI) instead of Basic Input/Output System (BIOS)

## Slide 40
Hardware Basics
PC Bootup Sequence
A Simple OS Example
Kernels

## Slide 41: What Happens After You Push Power?
A lot happens in between
  Pushing power…
  … And arriving at the desktop
Basic steps
  Start the BIOS
  Load settings from CMOS
  Initializing devices
  Run POST
  Initiate the bootstrap sequence

## Slide 42: Starting the BIOS
Basic Input/Output System (BIOS)
  A mini-OS burned onto a chip
Begins executing a soon as a PC powers on
  Code from the BIOS chip gets copied to RAM at a low address (e.g. 0xFF)
  jmp 0xFF (16 bits) written to RAM at 0xFFFF0 (220-16)
  x86 CPUs always start with 0xFFFF0 in the EIP register
Essential goals of the BIOS
  Check hardware to make sure its functional
  Install simple, low-level device drivers
  Scan storage media for a Master Boot Record (MBR)
    Load the boot record into RAM
    Tells the CPU to execute the loaded code

## Slide 43: Loading Settings from CMOS
BIOS often has configurable options
  Values stored in battery-backed CMOS memory

## Slide 44: Initialize Devices
Scans and initializes hardware
  CPU and memory
  Keyboard and mouse
  Video
  Bootable storage devices
Installs interrupt handlers in memory
  Builds the Interrupt Vector Table
Runs additional BIOSes on expansion cards
  Video cards and SCSI cards often have their own BIOS
Runs POST test
  Check RAM by read/write to each address

## Slide 45: Bootstrapping
Problem: we need to find and load a real OS
BIOS identifies all potentially bootable devices
  Tries to locate Master Boot Record (MBR) on each device
  Order in which devices are tried is configurable
MBR has code that can load the actual OS
  Code is known as a bootloader
Example bootable devices:
  Hard drive, SSD, floppy disk, CD/DVD/Bluray, USB flash drive, network interface card

## Slide 46: The Master Boot Record (MBR)
Address |  | Description | Size (Bytes)
Hex | Dec. |  | 
0x000 | 0 | Bootstrap code area | 446
0x1BE | 446 | Partition Entry #1 | 16
0x1CE | 462 | Partition Entry #2 | 16
0x1DE | 478 | Partition Entry #3 | 16
0x1EE | 494 | Partition Entry #4 | 16
0x1FE | 510 | Magic Number | 2
 |  | Total: | 512
Special 512 byte file written to sector 1 (address 0) of a storage device
Contains
  446 bytes of executable code
  Entries for 4 partitions
Too small to hold an entire OS
  Starts a sequence of chain-loading

## Slide 47: Example Bootloader: GRUB
Grand Unified Bootloader
  Used with Unix, Linux, Solaris, etc.

## Slide 49
Hardware Basics
PC Bootup Sequence
A Simple OS Example
Kernels

## Slide 50: Status Check
At this point we understand:
  The basic building blocks of device I/O
  How memory is laid out
  Basic x86 instructions
  How the BIOS locates and executes a bootloader
What’s next?
  Let’s build a tiny OS for the bootloader to load

## Slide 51: Goals of Our Simple OS
APIs for device access
  Read from the keyboard
  Read and write to a simple disk
  Display text to the screen
Ability to run a simple user program
A basic command line for running programs

## Slide 52: Sample Program 1 – Hello World
Writes “Hello World” to the frame buffer
Then loops forever
l
l
o
W
o
r
l
d
e
H
EBX
ECX
EDX
EAX
0xF000
H
11
H
He
Hel
Hell
Hello
Hello W
Hello Wo
Hello Wor
Hello Worl
Hello World
10
e
0xF001
9
l
0xF001
0xF002
0xF003
8
0xF004
7
o
0xF005
6
0xF006
5
W
0xF007
4
o
0xF008
3
r
0xF009
2
l
0xF00A
1
d
0xF00B
0
fbuf = 0xF000
str: 'Hello World'
begin: mov eax, str
mov ebx, 11
mov ecx, 0xF000
loop: mov edx, byte [eax]
inc eax
mov [ecx], byte edx
inc ecx
sub ebx, 1
jnz_loop done: jmp done

## Slide 53: Sample Program 1 – Hello World
In this program, there is no OS
  Program interacts directly with hardware
This approach might be used for highly-constrained, low-cost environments
  Example: simple embedded devices
In a system like this, the program is usually written into read-only-memory (ROM) at the factory

## Slide 54: Sample Program 2 – Keyboard to Screen
Reads input from the keyboard and writes it to the frame buffer
framebuf = 0xF000
status = 0xF800
keycode = 0xF801
begin: mov eax, 0xF000
loop: mov ebx, byte [0xF800]
cmp ebx, 0
jz loop
mov ebx, byte [0xF801]
mov [eax], byte ebx
inc eax
mov [0xF800], 0
jmp loop
How can we turn this functionality into an API?

## Slide 55: The x86 Stack
x86 CPU uses ESP register to implement a push down stack
Examples:
  push 0x01
  pop eax ; EAX = 1
Memory
0xCAFE | 0xAE
0x01 | 0xAA
 | 0xA6
 | 0xA2
 | 0x9E
 | 0x9A
 | 0x96
 | 0x92
 | 0x8E
 | 0x8A
 | 0x86
ESP

## Slide 56: Function Calls and the Stack
The stack is used to implement function calls
  call addr: call a function
    Calculates a return address (the address of the instruction following call)
    Pushes the return address on to the stack
    Jumps to addr (EIP = addr)
  ret: return from a function
    Pops the return address from the stack
    Jumps to the return address

## Slide 57: Function Call Example
…
10. push 2
11. push 1
12. call add
13. mov ecx, eax
…
20. add: mov eax, [esp + 4]
21. mov ebx, [esp + 8]
22. add eax, ebx
23. ret
Memory
0xCAFE | 0xAE
0x02 | 0xAA
0x01 | 0xA6
13 | 0xA2
 | 0x9E
ESP
EIP
Suppose we have code that calls
i = add(1, 2);

## Slide 58: Argument Ordering and Return Values
Function arguments are always pushed in reverse order
  Why?
  To support functions with a variable number of arguments
  Example: printf(“%i %f %s”, a, pi, str);
    Argument 1 tells you how many more arguments there are on the stack
By convention, return values are always placed in EAX
  This is why (typical) functions may only return one value

## Slide 59: Pop Quiz
…
27. call f
…
59. f: mov eax, [esp + 4]
…
Memory
10 | 0xAE
7 | 0xAA
28 | 0xA6
 | 0xA2
 | 0x9E
What does the stack look like after calling f(7, 10)?

## Slide 60: A Minimal Operating System
We’ll now write a simple OS that can:
  Read keyboard input
  Write it to the frame buffer
getkey()
  Loops until a key has been pressed
  Loads the key into EAX
getkey: mov edx, byte [status]
cmp edx, 0
jz getkey
mov [status], 0
mov eax, byte [keycode]
ret

## Slide 61: putchar()
putchar()
  Writes the 2 byte function argument to the frame buffer
  Maintains the frame buffer cursor
bufptr: variable holding a pointer to the frame buffer
putchar: mov eax, word [esp+ 4] mov ebx, dword [bufptr] mov [ebx], word eax add ebx, 1 mov [bufptr], ebx ret

## Slide 62: Using getkey() and putchar()
We can now rewrite Sample Program 2 using our simple OS
loop: call getkey push eax call putchar pop eax jmp loop
framebuf = 0xF000
status = 0xF800
keycode = 0xF801
begin: mov eax, 0xF000
loop: mov ebx, byte [0xF800]
cmp ebx, 0
jz loop
mov ebx, byte [0xF801]
mov [eax], byte ebx
inc eax
jmp loop
Old Code
New Code

## Slide 63: Why Do We Care?
Reusability
  Many programs can use getchar() and putchar()
Abstraction
  Programs don’t need to know details of the keyboard and frame buffer interfaces
Portability
  Program could run on another OS that supports getchar() and putchar()…
  … even if the hardware interface has changes

## Slide 64: Let’s Build a Basic Shell
Almost all OSes include a shell
  A program that takes commands from the user
  Earliest (and best) shells were command lines
  Modern shells are GUIs
Let’s build a shell into our OS
  Read a command line from the keyboard
  Read the associated program from the disk
  Load the program into memory and execute it

## Slide 65: Basic Program Loading
Memory regions are reserved
  Memory mapped hardware
  OS code
  IVT
  Etc…
To load and run a program:
  Read the program from disk into the program region of memory
  Use call to jump to the first instruction of the program
    Called the entry point
IVT
0x0000
0xFFFF
Main Memory
getchar()
User Program Region
Hardware
OS Code
putchar()

## Slide 66: Example Disk Controller
Disk drive interface
  Reads and writes occur in 512-byte blocks
  Block numbers start at 0
To write to block B
  Copy the data into range 0xF900 – 0xFAFF
  Write B to 0xF822
  Write ‘W’ to 0xF820
    Tells the drive to write the buffer
  Drive will write 0 to 0xF820 when the transfer is complete
Address | Purpose
0xFAFF | 512-byte buffer
… | 
0xF900 | 
0xF822 | block address
0xF820 | cmd/status

## Slide 67: Example Disk Controller (cont.)
To read from block B
  Write B to 0xF822
  Write ‘R’ to 0xF820
    Tells the drive to read data from the disk into the buffer
  Drive will write 0 to 0xF820 when the transfer is complete
  Data from B is now available in 0xF900 – 0xFAFF
Address | Purpose
0xFAFF | 512-byte buffer
… | 
0xF900 | 
0xF822 | block address
0xF820 | cmd/status

## Slide 68: Additional OS APIs
Assume we have already implemented some functions
  read_disk_block() reads a block from the disk to some address in memory
  getline() reads a line from the keyboard and stores it into a buffer

## Slide 69: Basic File System
Assume the disk is divided into blocks
We introduce a trivial file system
  Block 0 is the directory mapping of the file system
  Other blocks are program data blocks
Valid? | Name | Addr | len
1 | “file1.txt” | 1 | 2
0 |  |  | 
1 | “program.com” | 3 | 3
Block 0 (directory)
file1.txt
Blocks 1 and 2
program.com
Blocks 3, 4 and 5

## Slide 70: File System Structures
struct dirent {
bool valid;
char name[16]; int start; int len;
};
struct dirent directory[BLK_SIZ/sizeof(struct dirent)]
read_disk_block(/*blk #*/ 0, /*destination*/ directory);
Valid? | Name | Addr | len
1 | “file1.txt” | 1 | 2
0 |  |  | 
1 | “program.com” | 3 | 3
Block 0 (directory)
file1.txt
Blocks 1 and 2
program.com
Blocks 3, 4 and 5

## Slide 71: Basic Command Line
We can now write a very simple command line:
char buffer[80]; struct dirent directory[NDIR];
int i, start, count;
void *program_base = …; /* probably 0x100 or so */
while (1) {
getline(buffer);
read_disk_block(DIR_SECTOR, directory);
for (i = 0; i < NDIR; i++) {
if (strcmp(buffer,directory[i].name)== 0 && directory[i].valid) {
for (j = 0; j < directory[i].len; j++)
read_disk_block(/* block # */ directory[i].start + j, /* destination*/ program_base + j * 512);
break;
}
}
asm(“call program_base”);
/* returns here when program is done */
}

## Slide 72: Limitations of Our OS
Crashes if it can’t find the specified program
If the program crashes, the whole OS needs to be restarted
Programs may not run if the OS is upgraded
  Why?
  Programs access OS APIs directly
  What if the addresses change?
IVT
0x0000
0xFFFF
Main Memory
Hardware
getchar()
OS Code
putchar()
User Program

## Slide 73: System Call Interface
System call table
  Layer of indirection to abstract the OS APIs
  Table is always located at a fixed position
  Each OS API is given a specific index in the table
Programs access APIs via the table, instead of hard coding the function address

## Slide 74: Traps: Software Interrupts
Software can also generate interrupts
  Traps and exceptions are software interrupts
Example:
mov eax, 1 ; system call number goes in EAX, exit() = 1
xor ebx, ebx ; exit() takes one parameter
int 0x80 ; transfer control to the Linux kernel

## Slide 75: (Simplified) System Call Example
IVT
0x0000
0xFFFF
Main Memory
Interrupt Number | Pointer to Handler
0x80 | 0xA146
0xA146
0x80 Handler
User Program
mov eax, 1
xor ebx, ebx
int 0x80
Software executes int 0x80, pushes EIP
CPU looks up handler in the IVT
CPU transfers control to the OS handler
Handler looks up EAX in the syscall table
Jump to the API code
Syscall Table
printf()
OS Code
EAX | Pointer to API
1 | 0xC0F4
EIP
0xC0F4

## Slide 76: CPU Support for System Calls
Many CPUs provide instruction support for invoking system calls
  On x86, system calls are initiated via an interrupt
Example: Linux system calls
  On x86, int 0x80 is the system call interrupt
  EAX holds the table index of the desired API
EAX | Function
1 | sys_exit
2 | sys_fork
3 | sys_read
4 | sys_write

## Slide 77: Our OS So Far
Almost at the level of MS-DOS 1.0
Current features:
  Interface to frame buffer
  Interface to keyboard controller
  Interface to disk controller
  Command line
  Ability to load and execute simple programs
  Uses interrupts to make system calls

## Slide 78: Similarities with MS-DOS 1.0
Separate OS and program spaces
System call table accessed via interrupt
Command line is part of OS
Similar keyboard controller, frame buffer, and disk controller
IVT
0x0000
Top
Main Memory
MS-DOS
BIOS
User Program Region

## Slide 79
Hardware Basics
PC Bootup Sequence
A Simple OS Example
Kernels

## Slide 80: Towards a Kernel
“The one program running at all times on the computer” is the kernel
Typically loaded by the bootloader
Questions:
  What are the features that kernels should implement?
  How should we architect the kernel to support these features?

## Slide 81: Kernel Features
Device management
  Required: CPU and memory
  Optional: disks, keyboards, mice, video, etc.
Loading and executing programs
System calls and APIs
Protection and fault tolerance
  E.g. a program crash shouldn’t crash the computer
Security
  E.g. only authorized users should be able to login

## Slide 82: Architecting Kernels
Three basic approaches
  Monolithic kernels
    All functionality is compiled together
    All code runs in privileged kernel-space
  Microkernels
    Only essential functionality is compiled into the kernel
    All other functionality runs in unprivileged user space
  Hybrid kernels
    Most functionality is compiled into the kernel
    Some functions are loaded dynamically
    Typically, all functionality runs in kernel-space

## Slide 83: Monolithic Kernel
User Space
Kernel Space
Memory Manager
CPU Scheduling
Program Loader
Security Policies
Error Handling
System APIs
Device Drivers
File Systems
Monolithic Kernel Code
User Program

## Slide 84: Hybrid Kernel
User Space
Kernel Space
Memory Manager
CPU Scheduling
Program Loader
Security Policies
Error Handling
System APIs
File Systems
Kernel Code
Device Driver
Third-Party Code
Device Driver
File System
User Program

## Slide 85: Microkernel
User Space
Kernel Space
Memory Manager
CPU Scheduling
Interprocess Communication
Kernel Code
Networking Service
File System
Disk Driver
Network Card Driver
User Program 1
User Program 2

## Slide 86
Microkernels:
Small code base,
Few features
Monolithic Kernels:
Huge code base,
Many features
Hybrid Kernels:
Pretty large code base,
Some features delegated
Research Kernels:
Mach
L4
GNU Hurd
Kernels for Embedded System:
QNX

## Slide 87: Pros/Cons of Monolithic Kernels
Advantages
  Single code base eases kernel development
  Robust APIs for application developers
  No need to find separate device drivers
  Fast performance due to tight coupling
Disadvantages
  Large code base, hard to check for correctness
  Bugs crash the entire kernel (and thus, the machine)

## Slide 88: Pros/Cons of Microkernels
Advantages
  Small code base, easy to check for correctness
    Excellent for high-security systems
  Extremely modular and configurable
    Choose only the pieces you need for embedded systems
    Easy to add new functionality (e.g. a new file system)
  Services may crash, but the system will remain stable
Disadvantages
  Performance is slower: many context switches
  No stable APIs, more difficult to write applications